## Slide 1
DESIGNING D-FLIP FLOP USING VARIOUS CIRCUITS
BTP CODE : B24VRK01
A.KIRANMAI:S20210020251
T.RAJASEKHAR:S20210020325
Mentor: Dr. Ramesh Kumar

## Slide 2: Objectives:
Introduction of novel design approach for ternary D-flipflop
  Utilization of ternary buffer and two STIs with dual power supplies
Proposal of two hybrid architectures for ternary D-flipflop designs
  Combination of ternary buffer, STIs, and successor-predecessor circuits
Analysis of CNTFET and GNRFET outputs.

## Slide 3: Introduction of GNRFET
A GNRFET is fabricated by simply making connections between a channel of graphene nanoribbons and the metal contacts of source and the drain.
GNRFETs have garnered significant interest due to their potential for high carrier mobility, excellent electrical properties, and nanoscale
dimensions.
These transistors offer advantages such as
high on-off current ratios, high carrier
velocities, and potential compatibility
with existing silicon-based electronics.
GNRFET [5]

## Slide 4
The width (W) of GNR is calculated as
𝑊=(𝑁+1)(√3/2) 𝑎
Where, ‘N’ represents no of dimer lines which is proportional to width of GNR, a
is the lattice constant i.e., 0.142 nm.
Vth inversely proportional to width of GNR. No. of dimer lines is inversely proportional to energy band gap.
Parameters of GNRFET is nRib,n,L,Tox,sp,dop,p.
n=19
n=10

## Slide 5: Circuits:
    Designing D-Flip flop using Buffer and STI circuits:
    STI[2] PT STI[3] PTB STI[1]
    Existing Designs of Standard Ternary Inverter(STI)

## Slide 6
Modified STI Circuit Buffer Circuit
Here Ap and An are outputs of PTI and NTI
Vdd
Vdd/2
Gnd
A
A
Ap
An
(10,0)
(10,0)
(19,0)
(19,0)
Output
Vdd/2
Vdd
An
Gnd
Output
Ap
An
Ap
(19,0)
(19,0)
(10,0)
(10,0)
Vin | Buffer | STI
0 | 0 | 2
1 | 1 | 1
2 | 2 | 0

## Slide 7
Existing D-Flip Flop Design: Modified D-flip flop Design:
CLK
D
CLK
CLK
CLK
CLK
CLK
CLK
CLK
Ternary Buffer
STI
STI
Q
STI BASED D-FLIPFLOP[1]
Q+

## Slide 8: Output Waveforms:
CNTFET OUTPUT WAVEFORM

## Slide 9: Output Waveforms:
GNRFET OUTPUT WAVEFORM

## Slide 10
    Designing D-Flip flop using Successor and Predecessor circuits:
Existing Designs of Successor and Predecessor circuits
Successor Circuit[1]
Predecessor Circuit[1]

## Slide 11
Modified Successor Circuit Predecessor Circuit
Vdd
Gnd
Gnd
A
A
A
A
(10,0)
(19,0)
(19,0)
(10,0)
Output
Gnd
A
output
A
Vdd
1
(19,0)
(10,0)
(19,0)
A
Vdd
A
A
(10,0)
(19,0)
(10,0)
(19,0)
(19,0)
(19,0)
(19,0)
A
1
Vdd
Gnd
Vin | Successor | Predecessor
0 | 1 | 2
1 | 2 | 0
2 | 0 | 1
NTI
PTI

## Slide 12
Existing D-Flip Flop Design: Modified D-flip flop Design:
CLK
D
CLK
CLK
CLK
CLK
CLK
CLK
CLK
Q
Successor
Predecessor
Successor
Predecessor
D-flip flop using successor and predecessor circuits[1]
Q+

## Slide 13: Output Waveforms:
CNTFET OUTPUT WAVEFORM
GNRFET OUTPUT WAVEFORM

## Slide 14
  D-FLIP FLOP USING BUFFER AND SUCCESSOR PREDECESSOR CIRCUITS [HYBRID CIRCUIT]:
CLK
D
CLK
CLK
CLK
CLK
CLK
CLK
CLK
Q
Successor
Predecessor
Ternary Buffer
  We designed hybrid circuits by combining buffer , successor and predecessor circuits to analyse the quantities Power consumption and delay of circuit.
Q+

## Slide 15: Output Waveforms:
CNTFET OUTPUT WAVEFORM
GNRFET OUTPUT WAVEFORM

## Slide 16
  D-FLIP FLOP USING SUCCESSOR PREDECESSOR AND STI CIRCUITS [HYBRID CIRCUIT]
CLK
D
CLK
CLK
CLK
CLK
CLK
CLK
CLK
Q
Successor
Predecessor
STI
STI
  We designed hybrid circuits by combining successor ,predecessor circuits and STI circuits to analyse the quantities Power consumption and delay of circuit.
Q+

## Slide 17: Output Waveforms:
CNTFET OUTPUT WAVEFORM
GNRFET OUTPUT WAVEFORM

## Slide 18: CNTFET VS GNRFET
Comparison of Power(W)
Circuit | CNTFET | GNRFET
D-FLIP FLOP USING BUFFER AND STI CIRCUITS | 1.0712e-06 | 1.6326e-06
D-FLIP FLOP USING SUCCESSOR PREDECESSOR CIRCUITS | 6.5782e-08 | 3.3997e-06
D-FLIP FLOP USING BUFFER AND SUCCESSOR PREDECESSOR CIRCUITS | 1.0683e-06 | 3.4255e-06
D-FLIP FLOP USING SUCCESSOR PREDECESSOR AND STI CIRCUITS | 1.0894e-06 | 3.4255e-06

## Slide 19: CNTFET VS GNRFET
Comparison of Propagation Delay(sec)
Circuit | CNTFET | GNRFET
D-FLIP FLOP USING BUFFER AND STI CIRCUITS | 3.5257e-08 | 3.5307e-08
D-FLIP FLOP USING SUCCESSOR PREDECESSOR CIRCUITS | 3.5433e-08 | 3.6961e-08
D-FLIP FLOP USING BUFFER AND SUCCESSOR PREDECESSOR CIRCUITS | 3.5277e-08 | 3.5325e-08
D-FLIP FLOP USING SUCCESSOR PREDECESSOR AND STI CIRCUITS | 3.5258e-08 | 3.5314e-08

## Slide 20: Conclusion:
The simulated results obtained for the CNTFET and GNRFET structures for D-Flip Flop suggests that CNTFET structures can be possible low power alternative in sub nanometer regime.
CNTFET threshold voltage can be controlled by diameter which depends on the chirality vector. In GNRFET threshold voltage can be controlled by width which depends on number of dimer lines.
The design process utilizes different techniques in terms of transistor arrangement, two power supplies (Vdd, Vdd/2), transistor count reduction to reach the final target.
Clock overlapping[4]
CLK and CLK both low for a short period of time (the overlap period), both sampling pass transistors conduct and there is a direct path from the D input to the Q output.

## Slide 21: TIMELINE:
1
Literature Review and implemented some basic ternary inverters circuits and basic building blocks needed to improvise D-Flipflops.
2
Building D-flipflops using buffer-STI and successor-predecessor circuits (CNTFET and GNRFET)
3
New idea of design for D flipflop that avoids zero-zero overlapping and 1-1 overlapping.
4
Trying to design single phase clock in designing D-flip flop and try to design TSPC.

## Slide 22: References:
[1] K.RahbariandS.A.Hosseini,“NovelternaryD-flip-flap-flopandcounter based on successor and predecessor in nanotechnology,” AEU- Int. J. Electron. Commun., vol. 109, pp. 107–120, Sep. 2019.
[2] T. Sharma and L. Kumre, “Design of unbalanced ternary counters using shifting literals based D-Flip-Flops in carbon nanotube technology,” Com put. Elect. Eng., vol. 93, 2021, Art. no. 107249.
[3] S. Gadgil and C. Vudadha, “Design of CNFET-based low-power ternary sequentiallogiccircuits,”inProc.IEEE21stInt.Conf.Nanotechnol.,2021, pp. 169–172.
[4]Chen YY, Sangai A, Gholipour M, Chen D. Graphene nano-ribbon field-effect transistors as future low power devices. Proc Int Symp Low Power Electron Des. 2013;151–6.
[5]Venkataiah C.1, Mallikarjuna Rao Y.2, “Performance analysis of Ternary Adder and Ternary Multiplier without using Encoders and Decoders” April 2021 IEEE Access 9(April):1.

## Slide 23: THANK YOU